## Slide 1
UNDERWATER ACOUSTICS
The Theory of Sound in Water
Transmit power and intensity · the single beam · directivity, gain and equivalent beam angle

## Slide 2
ACOUSTIC FUNDAMENTALS
A wave that travels near 1,500 m/s
Sound moves through water as a pressure wave. Its speed, frequency and wavelength are linked by one identity — and the speed itself depends on the water's own properties.
Wave relationship
λ
c = f × λ
c = speed (m/s) f = frequency (Hz) λ = wavelength (m)
TYPICAL VALUE
~1,500 m/s
in near-surface seawater — roughly 4.3× faster than in air
BUT IT VARIES WITH
T
Temperature
dominant near-surface driver
S
Salinity
raises density and stiffness
P
Pressure / depth
compresses the water
02

## Slide 3
ACOUSTIC FUNDAMENTALS
From transmit power to acoustic intensity
The transceiver drives the transducer with an electrical transmit power. What actually propagates through the water is intensity — energy flow per unit area — almost always expressed in decibels.
I
Acoustic Intensity
I = p² / (ρc)
p = acoustic pressure (Pa), ρ = water density (kg/m³), c = sound speed (m/s). Intensity is power flowing through a unit area, in watts per square metre (W/m²).
Near the source, intensity relates directly to transmit power. Farther out, spreading and absorption reduce it with range.
SL
Source Level
SL = 10 log₁₀(I₁ₘ / I_ref)
The intensity produced at a 1 m reference range, expressed in decibels above a fixed reference intensity — the standard way transmit strength is quoted.
THE DECIBEL SCALE
Every ×10 rise in power adds +10 dB — a 10× more powerful transmitter is 10 dB louder, 100× is 20 dB louder.
03

## Slide 4
ACOUSTIC FUNDAMENTALS
Two losses shrink every signal
As sound travels, it loses energy two ways: the wavefront spreads geometrically, and the medium absorbs energy — with absorption rising steeply at higher frequencies.
Source
Spherical spreading: intensity falls as 1 / R²
One-way transmission loss (TL)
TL = 20 log₁₀(R) + αR
Absorption coefficient (α) vs. frequency
Chart: 
| 18 kHz | 38 kHz | 70 kHz | 120 kHz | 200 kHz | 333 kHz | 500 kHz
Absorption (dB/km) | 1.5 | 3.5 | 6.6 | 20 | 40 | 87 | 140
04

## Slide 5
SENSING THE WATER COLUMN
The single-beam transducer
A transducer concentrates transmitted energy into a directional beam rather than radiating equally in all directions. A single-beam system uses one such beam to sound the water column beneath it.
Transducer
θ
main lobe
side lobe
side lobe
half-power beamwidth
1
Main lobe
Carries almost all transmitted energy — the beam's axis of maximum sensitivity.
2
Beamwidth (θ)
Angular width of the main lobe, usually taken at the half-power points.
3
Side lobes
Small off-axis leakage; strong reflectors there can create weak false echoes.
4
Single-beam limit
Range and echo strength along the axis only — not a target's position within the beam.
05

## Slide 6
BEAM PERFORMANCE
Directivity concentrates energy — gain measures it
A larger transducer face packs the same energy into a narrower beam. That concentration, relative to a hypothetical source radiating equally in all directions, is what directivity and gain describe.
Aperture size sets beam width
Small aperture
wide beam → low gain
Large aperture
narrow beam → high gain
Directivity factor D compares the on-axis intensity to that of an omnidirectional source radiating the same total power. A narrower main lobe means a higher D.
G
Transducer Gain
G = 10 log₁₀(D)
Gain expresses directivity in decibels — the standard figure of merit quoted for a transducer's on-axis performance, both transmitting and receiving.
TWO-WAY GAIN
An echo passes through the beam twice — out and back — so the same gain applies on transmit and receive, for a combined 2G in decibels.
06

## Slide 7
BEAM PERFORMANCE
Equivalent beam angle: one number for a beam's shape
A real beam tapers gradually from its peak; there is no sharp edge to say where it “ends.” The equivalent beam angle Ψ replaces that taper with an idealized beam of the same peak response and the same total energy.
Two-way beam response vs. angle off-axis
peak response
actual beam
equivalent (Ψ)
off-axis angle →
Same peak height, same area under the curve — different shape.
Ψ
Expressed in steradians (solid angle), or as 10 log₁₀(Ψ) in dB re 1 steradian.
WHY IT MATTERS
It converts a single target's echo into the backscattering strength of an entire volume of scatterers, by defining how much of the water column each ping effectively samples.
A calibrated constant, unique to each transducer.
07

## Slide 8
SUMMARY
Six ideas behind every single-beam measurement
1
Sound is a pressure wave: c = f × λ, travelling near 1,500 m/s and varying with temperature, salinity and pressure.
2
Transmit power sets the acoustic intensity radiated; because intensity spans huge ranges, it is expressed in decibels (Source Level).
3
Transmission loss combines geometric spreading with frequency-dependent absorption as the signal travels out and back.
4
A single-beam transducer concentrates energy into one main lobe — giving range and echo strength, but not off-axis position.
5
Directivity and gain (G = 10 log₁₀ D) quantify how tightly a transducer's aperture concentrates energy on-axis.
6
The equivalent beam angle Ψ reduces a real beam's taper to one calibrated number, used to convert echoes into volume backscattering strength.