## Slide 1
UNDERWATER ACOUSTICS · SCIENTIFIC ECHO SOUNDING
Sound in Water
and the Kongsberg EK80 Echo Sounder System
From acoustic first principles to wideband, calibrated ocean sensing
Prepared as a technical briefing

## Slide 2
THE PHYSICAL CASE FOR SOUND
Why the ocean is explored with sound
Electromagnetic waves — light, radar, radio — are absorbed by seawater within meters. Mechanical pressure waves (sound) travel through water with comparatively little loss, making acoustics the only practical way to sense range, depth and structure across an entire water column.
Rule of thumb: light in seawater is useful to tens of meters; sound is useful to thousands.
Usable sensing range in open ocean (illustrative)
Chart: 
| Radio / Radar | Visible Light | Sound (Sonar)
Range | 0.5 | 30 | 3000
Log-scale effective range in meters — order-of-magnitude comparison, not a measurement.
02

## Slide 3
ACOUSTIC FUNDAMENTALS
The speed of sound is not constant
Sound travels through seawater roughly 4.3 times faster than through air. The exact speed at any point depends on three properties of the water itself:
T
Temperature
The dominant factor near the surface — warmer water raises sound speed.
S
Salinity
Higher salt content increases density and stiffens the medium, raising speed.
P
Pressure / Depth
Increasing pressure with depth compresses water and raises speed.
TYPICAL VALUE
~1,500
metres per second, near-surface ocean water
A widely used approximation (Mackenzie, 1981):
c ≈ 1449.2 + 4.6T − 0.055T² + 1.39(S−35) + 0.017D
T = temperature (°C) S = salinity (PSU) D = depth (m)
03

## Slide 4
ACOUSTIC FUNDAMENTALS
A layered ocean bends sound rays
Because sound speed varies with depth, acoustic rays refract toward slower-speed layers — just as light bends between media. The resulting sound-speed profile (SSP) determines how far and in what direction acoustic energy actually travels, and must be measured to correct echosounder ranges.
Typical mid-latitude sound-speed profile
Chart: m/s
| 0 m | 100 m | 300 m | 600 m | 1000 m | 1500 m | 2000 m
Sound speed | 1541 | 1507 | 1495 | 1487 | 1483 | 1488 | 1496
1
Mixed layer
Near-uniform speed; wind-mixed, can trap sound near the surface (surface duct).
2
Thermocline
Temperature falls quickly with depth, so speed falls quickly — rays refract downward.
3
Deep isothermal layer
Below the thermocline, temperature stabilizes and rising pressure slowly increases speed again — forming the deep sound (SOFAR) channel minimum.
04

## Slide 5
ACOUSTIC FUNDAMENTALS
Higher frequency, shorter reach
Seawater absorbs acoustic energy through chemical relaxation and viscosity, and absorption rises steeply with frequency. This is the central trade-off in echosounder design: low frequencies travel far with coarse resolution; high frequencies resolve fine detail over short range.
Design consequence: EK80 spans 10–500 kHz precisely so operators can trade range against resolution by choosing frequency.
Absorption coefficient vs. frequency (illustrative, seawater)
Chart: 
| 18 kHz | 38 kHz | 70 kHz | 120 kHz | 200 kHz | 333 kHz | 500 kHz
Absorption (dB/km) | 1.5 | 3.5 | 6.6 | 20 | 40 | 87 | 140
05

## Slide 6
ACOUSTIC FUNDAMENTALS
Two losses shrink every echo
As a pulse travels out and its echo returns, energy is lost twice over: geometric spreading as the wavefront expands, and absorption as the medium dissipates energy to heat. Together these define the sonar equation's transmission loss term.
Transducer
Spherical spreading: intensity falls as 1 / R²
One-way transmission loss
TL = 20 log₁₀(R) + αR
20 log₁₀(R)
Geometric spreading loss — grows with the log of range R.
αR
Absorption loss — grows linearly with range, scaled by the frequency-dependent absorption coefficient α.
× 2
Applied twice in an echosounder: once outbound, once on the returning echo (two-way TL).
06

## Slide 7
HOW AN ECHOSOUNDER WORKS
Range from a single number: time
An echosounder transmits a short acoustic pulse and measures the time until its echo returns. Because the sound speed c is known, that round-trip time converts directly to range.
sea surface
Transducer
outgoing pulse
returning echo
target (e.g. fish)
R
R = c × t / 2
c = sound speed, t = round-trip time
seabed
WORKED EXAMPLE
An echo returns 0.133 s after transmission, in water where c ≈ 1500 m/s.
R = (1500 × 0.133) / 2
≈ 100 metres
This range/time relationship, repeated thousands of times per survey line, is what an echosounder ultimately measures.
07

## Slide 8
HOW AN ECHOSOUNDER WORKS
Not just where — what, and how much
Range alone locates a target. The strength of its echo carries information about size, composition and abundance — the basis of quantitative fisheries acoustics.
TS
Target Strength
A single object's echo, expressed in dB. Larger, denser, or better-oriented targets (e.g. a fish's swim bladder) return a stronger echo — used to estimate individual fish length.
Sv
Volume Backscattering
The combined echo from many scatterers in a sampled volume of water — zooplankton, fish schools, bubbles — used to estimate biomass density.
θ/φ
Beam Geometry
A split-beam transducer also recovers each echo's angular position in the beam, enabling single-target tracking and precise TS measurement.
08

## Slide 9
THE KONGSBERG EK80 SYSTEM
From single frequencies to a wideband instrument
The Simrad EK80, built by Kongsberg, is a scientific echo sounder and ADCP system that succeeded the EK60 — for decades the international standard for fish-stock assessment. Where the EK60 sampled a handful of fixed frequencies, the EK80 processes a continuous frequency band on every transducer, sweeping far more acoustic information out of the same water column.
Modular system: multiple transceivers and transducers operate through one operator station
Backward-compatible with EK60-era General Purpose Transceivers (GPT) as well as new Wide Band Transceivers (WBT)
A vessel-mounted system typically runs six transducers, each covering a different part of the band
OPERATIONAL RANGE
10–500
kilohertz, spanned simultaneously across the system's transducers
PREDECESSOR
Simrad EK60 — over 1,100 units sold to research vessels worldwide; an upgrade path exists for EK60 vessels moving to EK80.
09

## Slide 10
THE KONGSBERG EK80 SYSTEM
The wideband idea: resolution without a short pulse
Classic narrowband sonars trade range resolution for signal energy — a shorter pulse resolves finer detail but carries less energy, and vice-versa. EK80's wideband (FM “chirp”) mode breaks that trade-off.
CW
Narrowband (CW)
Single fixed frequency per pulse
Range resolution set only by pulse duration
Compatible with legacy EK60 data time-series
Limited frequency information for target ID
FM
Wideband (FM chirp)
Frequency swept continuously across a band
Resolution set by bandwidth, not pulse length
Strong signal-to-noise from pulse compression
Continuous frequency response aids species/target classification
10

## Slide 11
THE KONGSBERG EK80 SYSTEM
System architecture, end to end
1
Transducer(s)
Converts electrical signal to sound and back. EK80 supports single- and split-beam transducers across the 10–500 kHz band — typically several per vessel.
2
Transceiver
Generates the transmit pulse and digitizes the returning echo. Works with legacy General Purpose Transceivers (GPT) or new Wide Band Transceivers (WBT).
3
Operator Software
One station controls every transceiver/transducer pair, applies calibration, and displays echograms, TS and Sv in real time.
4
Raw Data & Post-Processing
Full time-series raw data is stored for replay, and is compatible with third-party post-processing tools for survey analysis and reporting.
›
›
›
11

## Slide 12
APPLICATIONS
One acoustic platform, many ocean questions
⚙
Fish Stock Assessment
The original and primary use: quantitative biomass and abundance estimates that underpin fisheries management worldwide.
◈
Ecosystem Monitoring
Continuous frequency response across the water column supports broader biological and habitat monitoring beyond single-species surveys.
≈
Physical Oceanography
Wideband, low-frequency capability extends EK80 use into physical and chemical oceanography — e.g. tracking gas seep plumes rising from the seafloor.
△
Seabed & Habitat Mapping
Split-beam geometry and calibrated backscatter support bottom characterization alongside water-column work.
12

## Slide 13
SUMMARY
Sound is the ocean's only long-range signal — and EK80 reads it precisely
1
Sound speed (~1,500 m/s) varies with temperature, salinity and pressure, bending propagation paths through the water column.
2
Frequency governs the fundamental trade-off between range (low frequency) and resolution (high frequency).
3
Echosounders measure range from round-trip travel time, and echo strength (TS/Sv) from amplitude.
4
EK80 replaces fixed-frequency sensing with a wideband 10–500 kHz architecture, decoupling resolution from pulse length and improving target characterization across fisheries, ecosystem and oceanographic applications.
Sources: Kongsberg / Kongsberg Discovery product documentation and press materials.